## Slide 1: Lab 3
Akshati Vaishnav

## Slide 2: Reformatting the Baseline
Converting baseline into functions
Combined k1 and k2 loops because they used the same set of arrays
1.13x speedup from baseline

## Slide 3: Unrolls, pipelining, streaming, and dataflow
Processing 16 elements at once
4218 cycles
7.918 ns
Utilization (%): 72| 17| 10| 52| 0|
Speedup = 275x
FIFO usage was blowing up:
  Choosing stream sizes carefully
  Aggregate pragma: groups all elements of stream into a single-wide vector with bit-alignment so that members can be read and written to simultaneously
    Caused some utilization changes, but it didn’t change the speedup

## Slide 4: Unrolls, pipelining, streaming, and dataflow

## Slide 5: Increasing elements in vector
Maximum elements we can process through bus is 1024
Processing 32 elements at once
2165 cycles
8.834 ns
Speedup = 481x
Have reached the limit of using a wide bus

## Slide 6: Changing Clock Period in Tcl Script
Changed it to 2.5ns
2201 cycles
2.484 ns
|Utilization (%) | 52| 35| 38| 85| 0|
Speedup: 1683x

## Slide 7: Decreasing Data Type Sizing
Trial and error
Script clock period: 2ns
2188 cycles
1.982 ns
Speedup: 2122x

## Slide 8: Adder tree
Addition in the k1_k2 function was slowest
Converted tmp_sum to be a separate loop with four levels of adders

## Slide 9: Adder tree
Addition in the k1_k2 function was slowest
Converted tmp_sum to be a separate loop
Used complete array partitioning
  Utilization was low

## Slide 10: Minor Updates
Changing divisions to constants/multiplication/bit shifts when possible
Moving division to be at FIFO insertion time

## Slide 11: Final Numbers
Script clock period: 2ns
2138 cycles
1.906ns clock period
2259x period

## Slide 12: LLM Usage
Adder tree coding

## Slide 13: Code